## Slide 1: Python Flowgraphs
Shane Flandermeyer1,2
1Advanced Radar Research Center, University of Oklahoma, Norman, Oklahoma, USA
2School of Electrical and Computer Engineering, University of Oklahoma, Norman, OK, USA

## Slide 2: Python Flowgraphs
Once you have created a flowgraph in companion, you can use the toolbar to generate a Python file that allows you to run the flowgraph from the command line!
To run this file, change into its directory and execute the command:
$ python3 filename.py *
* Dollar sign indicates a command line input; no need to type it
Let’s look at the Python for a simple flowgraph that generates a real sinusoid and displays the signal in the time domain

## Slide 3: Python Flowgraphs
When you open the generated Python file, the first line you’ll see is
#!/usr/bin/env python3
  Specifies the path to your Python interpreter
  If the file runs on your computer but not on someone else’s, this may be why
The next block of code is a comment about the license/copyright.
  Not important to us unless there’s a specification for public release

## Slide 4: Python Flowgraphs
The first block of actual code is
if __name__ == '__main__':
import ctypes
import sys
if sys.platform.startswith('linux'):
try:
x11 = ctypes.cdll.LoadLibrary('libX11.so')
x11.XInitThreads()
except:
print("Warning: failed to XInitThreads()")
  Initializes the threads for each block
  You should not touch this

## Slide 5: Python Flowgraphs
Next up are the import statements. Most of these will vary depending on your flowgraph’s function, but the two most important ones are
from gnuradio import gr
  Necessary for any kind of GNU Radio application. Without it, your flowgraph will not run
from gnuradio import blocks
  Allows us to use the gr-blocks library, AKA the largest Library of GNU Radio components

## Slide 6: Python Flowgraphs
Now we define a class for our flowgraph
class my_flowgraph(gr.top_block, Qt.QWidget):
Inherits from two parent classes
  top_block: A top-level container for our flowgraph
    Provides implementation for start/stop and lock/unlock (for thread safety) operations
  QWidget: A base class for all QT-based UI objects
    Used here to generate our GUI window
    We’ll cover this in much more detail in our discussion of GUI blocks

## Slide 7: Python Flowgraphs
The flowgraph’s constructor comes after the class declaration
def __init__(self):
Most of the code in here simply declares variables and sets up the GUI window, so we can safely ignore those parts
The sections that we care about are those titled Blocks and Connections
  To instantiate a block in python, use the following format:
  self.{block_variable_name} = {block_module}.{ block_name( {parameters} ) }
  So for our signal generator block, the syntax would be
  self.sig_source = analog.sig_source_f(samp_rate,analog.GR_COS_WAVE,1000,1,0,0)

## Slide 8: Python Flowgraphs
The flowgraph’s constructor comes after the class declaration
def __init__(self):
Most of the code in here simply declares variables and sets up the GUI window, so we can safely ignore those parts
The sections that we care about are those titled Blocks and Connections
  To instantiate a block in python, use the following format
  self.{block_variable_name} = {block_module}.{ block_name( {parameters} ) }
  So for our signal generator block, the syntax would be
  self.sig_source = analog.sig_source_f(samp_rate,analog.GR_COS_WAVE,1000,1,0,0)
Variable Name

## Slide 9: Python Flowgraphs
The flowgraph’s constructor comes after the class declaration
def __init__(self):
Most of the code in here simply declares variables and sets up the GUI window, so we can safely ignore those parts
The sections that we care about are those titled Blocks and Connections
  To instantiate a block in python, use the following format
  self.{block_variable_name} = {block_module}.{ block_name( {parameters} ) }
  So for our signal generator block, the syntax would be
  self.sig_source = analog.sig_source_f(samp_rate,analog.GR_COS_WAVE,1000,1,0,0)
Module Name

## Slide 10: Python Flowgraphs
The flowgraph’s constructor comes after the class declaration
def __init__(self):
Most of the code in here simply declares variables and sets up the GUI window, so we can safely ignore those parts
The sections that we care about are those titled Blocks and Connections
  To instantiate a block in python, use the following format
  self.{block_variable_name} = {block_module}.{ block_name( {parameters} ) }
  So for our signal generator block, the syntax would be
  self.sig_source = analog.sig_source_f(samp_rate,analog.GR_COS_WAVE,1000,1,0,0)
Specific block name

## Slide 11: Python Flowgraphs
The flowgraph’s constructor comes after the class declaration
def __init__(self):
Most of the code in here simply declares variables and sets up the GUI window, so we can safely ignore those parts
The sections that we care about are those titled Blocks and Connections
  To instantiate a block in python, use the following format
  self.{block_variable_name} = {block_module}.{ block_name( {parameters} ) }
  So for our signal generator block, the syntax would be
  self.sig_source = analog.sig_source_f(samp_rate,analog.GR_COS_WAVE,1000,1,0,0)
(positional) block arguments

## Slide 12: Python Flowgraphs
Once the blocks are instantiated, we need to connect them.
These connections go into the Connections section, and the syntax for connecting blocks is as follows:
self.connect( ({block1}, {output_port}), ({block2}, {input_port}) )
For our flowgraph, the connections section will look something like:
self.connect( (self.sig_source, 0), (self.throttle, 0) )
self.connect( (self.throttle, 0), (self.time_sink, 0) )
  In words: connect the 0th output of the source to the 0th input of the throttle, then connect the 0th output of the throttle to the 0th input of the source.
  Important: Port numbers are zero indexed
  Port numbering is block specific (i.e. each block with n inputs and n outputs has an input 0,1,…,n and output 0,1,…,n)

## Slide 13: Python Flowgraphs
The previous discussion covers just about everything we need to care about in Python flowgraph files
  There is a main function below the flowgraph class, but there is nothing there for us to modify
If the process seems time consuming, that’s because it is.
  Imagine the code necessary for flowgraphs with >20 blocks with multiple inputs and outputs!
  BIG TAKEAWAY: Let companion handle as many gritty details as possible, and only move to Python when you have no other choice (e.g. QA tests)
C++ flowgraph files also exist, but they don’t offer a tangible performance improvement (and you have to deal with C++)